## Slide 1
Data Saves Lives
The Story of Safety Testing: How Tragedy, Science, and Data Created the Modern Safety Ecosystem

## Slide 2
77%
Reduction in traffic fatality rate since 1970
1970: 4.74 deaths per 100M miles | Today: 1.10 deaths per 100M miles If we still had 1970 rates with today's driving: 153,000 deaths per year instead of 36,000

## Slide 3
The Pattern: Every Test Has a Story
Every crash test exists because people were dying in a specific way
The cycle repeats throughout history:
  TRAGEDY: People die in ways we don't understand
  PIONEERS: Researchers ask 'why?' and investigate
  DATA: Testing reveals the mechanism of injury
  INSTITUTION: Regulatory body is formed or empowered
  STANDARD: A test is created to measure the problem
  ENGINEERING: Manufacturers design solutions
  LIVES SAVED: That specific death mode decreases
Then a NEW gap emerges... and the cycle continues
This presentation traces that cycle from 1899 to today

## Slide 4
Part 1: The Dark Ages
1899-1965: When No One Was Watching

## Slide 5
Before Safety: The Philosophy of Blame
1899: First US traffic death - Henry Bliss, hit by electric taxi in NYC
1921: 13,253 deaths with 55 billion VMT (24.09 deaths per 100M miles)
1937: 37,819 deaths - 14x today's fatality RATE
Industry position: 'Crashes are caused by bad drivers, not bad cars'
The Three E's of traffic safety:
  Education (teach drivers to be careful)
  Enforcement (punish bad drivers)
  Engineering (of ROADS, not vehicles)
Vehicle design was NOT considered a safety factor
No federal oversight. No standards. No data.
The car was fine. You were the problem.

## Slide 6
What Cars Were Like
No seatbelts (optional accessory, rarely ordered)
Rigid steering columns - metal shafts pointed at driver's chest
  By 1964: over 1 MILLION cumulative steering column deaths
Solid steel dashboards with chrome knobs and protrusions
No crumple zones - rigid structures transferred all force to occupants
No head restraints - whiplash was expected
Windshields of plate glass - shattered into deadly shards
Fuel tanks placed wherever convenient - often behind rear bumper
Door latches that popped open on impact - ejecting occupants
If you crashed, the car stayed intact. You didn't.

## Slide 7
The Pioneers
The individuals who changed everything

## Slide 8
Hugh DeHaven: The Father of Crashworthiness
1917: Survives mid-air collision as WWI pilot trainee - fell 500 feet
  Other pilot and his observer died. DeHaven walked away.
  Spent the rest of his life asking: 'Why did I survive?'
1942: Founded Cornell Crash Injury Research Project
Key insight: The 'Second Collision'
  First collision: car hits object
  Second collision: occupant hits interior
  The second collision is what kills people
Studied survivors of falls from great heights
  People survived 10-story falls if they landed on awnings
  Conclusion: 'Package the passenger' - distribute forces
His research led to padded dashboards, collapsible columns, door locks
Quote: 'The human body can tolerate far greater forces than we assumed - if distributed properly.'

## Slide 9
John Stapp: The Fastest Man on Earth
USAF Flight Surgeon, Physician, Biophysicist (1910-1999)
1947: Began rocket sled deceleration experiments at Edwards AFB
Problem: No one knew human tolerance limits for rapid deceleration
Solution: Stapp rode the sled himself - 29 TIMES
December 10, 1954: The final ride
  Reached 632 mph, stopped in 1.4 seconds
  46.2 g deceleration - still a record for voluntary human exposure
  Injuries: broken ribs, broken wrists, temporary blindness, lost fillings
Prior belief: Humans couldn't survive beyond 18g
Stapp proved: Proper restraints + force distribution = survival
His research led to aircraft seatbelts, ejection seats, auto restraints
Fun fact: 'Murphy's Law' originated on Stapp's project

## Slide 10
"I felt a sensation in the eyes, somewhat like the extraction of a molar without anesthetic."
-- John Stapp, describing 46.2g deceleration

## Slide 11
The Wayne State Cadaver Pioneers
1930s-1960s: Wayne State University, Detroit
Problem: How do we measure human injury tolerance without killing people?
Solution: Use cadavers - the recently deceased who donated bodies to science
Research methods:
  Ball bearings dropped on skulls (fracture thresholds)
  Bodies dropped from heights onto steel plates
  Crude accelerometers attached to measure forces
Professor Lawrence Patrick subjected HIMSELF to impacts
Created the Wayne State Tolerance Curve - foundation of HIC (Head Injury Criterion)
Albert King's 1995 calculation: Each cadaver saves 276 lives per year
  61 from seatbelt improvements
  147 from airbag design
  68 from windshield safety
Ethically controversial. Scientifically irreplaceable. Lives saved: hundreds of thousands.

## Slide 12
Nils Bohlin: The Seatbelt that Saved Millions
Swedish engineer (1920-2002), previously designed ejection seats at Saab
1958: Hired by Volvo as safety engineer
1959: Invented the modern 3-point seatbelt
  Previous seatbelts were 2-point lap belts - caused internal injuries
  The 3-point V-shape distributes force across chest AND pelvis
The remarkable decision:
  Volvo patented the design (US Patent 3,043,625)
  Then made it available to ALL automakers for FREE
  'Safety should not be proprietary'
Bohlin's study of 28,000 crashes:
  No belted occupant died below 60 mph if compartment stayed intact
NHTSA estimate: Seatbelts save ~15,000 lives per year in the US alone
One invention. One decision to share it freely. Millions of lives saved.

## Slide 13
Ralph Nader: Unsafe at Any Speed (1965)
November 30, 1965: A young lawyer publishes a book
Chapter 1: 'The Sporty Corvair' - exposed dangerous swing-axle suspension
Central thesis: Automakers prioritized STYLE over SAFETY
  $700 per car spent on annual styling changes
  $0.23 per car spent on safety
The GM Response:
  Hired private investigators to follow Nader
  Tapped his phones, tried to entrap him
  GM President forced to apologize before Congress
  Nader sued and won $425,000
The impact: Public awakening to automotive safety as a design problem
The book that launched federal regulation

## Slide 14
Part 2: The Birth of Regulation
1966-1980: Institutions Emerge

## Slide 15
The Regulatory Revolution
1966
National Traffic and Motor Vehicle Safety Act signed by President Johnson
1966
US Department of Transportation created
1966
William Haddon appointed first NHTSA Administrator
1967
First 20 FMVSS standards issued
1968
FMVSS 208 takes effect - seatbelts required
1968
36 football fatalities - leads to NOCSAE founding (1969)
1969
William Haddon becomes IIHS President - transforms into testing organization
1970
NHTSA established as independent agency
1976
Hybrid III dummy introduced - still the gold standard today
1979
NHTSA NCAP launched - first consumer crash test ratings

## Slide 16
William Haddon Jr.: Father of Injury Epidemiology
First NHTSA Administrator (1966-1969), then IIHS President (1969-1985)
Revolutionary insight: Crashes are PUBLIC HEALTH problems, not moral failures
Created the 'Haddon Matrix' - still used today:
  Pre-event factors (prevent crash)
  Event factors (reduce injury severity)
  Post-event factors (improve survival after crash)
Philosophy: Design systems assuming humans WILL make mistakes
  Don't blame the driver - engineer the solution
At IIHS: Transformed from insurance lobbying to TESTING organization
Pushed for standards, published data, held manufacturers accountable
Died 1985 at age 58 - but his framework shapes safety policy worldwide

## Slide 17
The Safety Ecosystem Emerges
Government/Regulatory
NHTSA (1970) - Federal Motor Vehicle Safety Standards
- Minimum requirements - pass/fail
- Mandatory compliance
- 70+ FMVSS standards today
Transport Canada
UN/ECE (Europe)
JNCAP, KNCAP, ANCAP, etc.
Consumer Testing (Independent)
IIHS (1959, testing from 1969)
- Insurance-funded
- Tests ABOVE minimum standards
- Star/letter ratings create market pressure
Euro NCAP (1997)
Global NCAP programs (2000s-present)
Key: Competition for ratings drives innovation

## Slide 18
IIHS: Where Insurance Meets Safety
Founded 1959 by insurance industry - they PAY crash claims
Business case: Fewer crashes = lower payouts = higher profits
1969: Haddon transforms IIHS into testing organization
Key innovations:
  1995: Moderate Overlap frontal test (40% offset)
  2003: Side Impact test with small female dummy
  2009: Roof strength ratings
  2012: Small Overlap test (25% offset) - shocked the industry
  2013: Front Crash Prevention (AEB) testing
  2021: Updated side test - heavier, taller barrier
IIHS tests are often MORE demanding than NHTSA requirements
Manufacturers compete for 'Top Safety Pick' - market pressure works

## Slide 19
NOCSAE: Sports Safety After Tragedy
1968: 36 football players died - worst year on record
  Most from head and neck injuries
  No standards for helmets - manufacturers made their own claims
1969: NOCSAE founded (National Operating Committee on Standards for Athletic Equipment)
1973: First football helmet certification standard
  Drop tower test: helmet on headform dropped onto anvil
  Severity Index (SI) must be below 1200
Results:
  1960s: 26 deaths/year
  1970s: 15 deaths/year (standards take effect)
  2010s: 3 deaths/year
90% reduction in football fatalities from better helmet standards
Same basic physics as automotive: protect the brain from deceleration

## Slide 20
Euro NCAP: Forcing Safety in Europe (1997)
European governments struggled to mandate safety improvements
Solution: Consumer information creates market pressure
1997: First Euro NCAP ratings published
Immediate impact: Rover 100 receives 1 star (out of 4)
  Rover pulls the car from production within MONTHS
  Proved consumer ratings could kill unsafe products
Euro NCAP has consistently pushed ahead of regulation:
  Pedestrian protection testing (1997)
  AEB requirement for 5-star (2014)
  Driver monitoring requirement (2024)
  Night pedestrian testing (2024)
The model: Make safety a COMPETITIVE advantage, not just compliance
Euro NCAP tests things the US still doesn't require.

## Slide 21
Part 3: Test Modes
Each test exists because people were dying a specific way

## Slide 22
Frontal Impact Testing
Where it all began

## Slide 23
FMVSS 208: Occupant Crash Protection
NHTSA | Introduced: 1968
PURPOSE
The foundational standard for frontal crash protection. Initially required only seatbelt anchorages. Today includes 30 mph full frontal barrier test, driver and passenger airbag requirements, and advanced occupant sensing. This single standard drove development of seatbelt systems, frontal airbags, and all advanced restraint systems.
KEY MEASUREMENTS
Head acceleration (HIC15 < 700)
Chest acceleration (3ms clip < 60g)
Chest deflection (< 63mm for 50th male)
Femur load (< 10 kN)
Neck injury criteria (Nij < 1.0)
DTS CONNECTION
DTS accelerometers in head, chest, pelvis. Load cells in neck, femur, tibia. Chest deflection potentiometers. These measurements define whether a vehicle passes. Every data point matters - one bad channel could mean repeating a $500K test.

## Slide 24
The Airbag Wars: 28 Years of Fighting
1970
NHTSA proposes airbag requirement
1972
GM offers airbags on Oldsmobiles - few buyers
1976
Industry lobbying delays requirement
1977
Joan Claybrook (NHTSA) pushes airbag mandate
1981
Reagan administration RESCINDS mandate
1983
Supreme Court rules rescission was arbitrary
1984
Compromise: 'automatic restraint' - airbag OR automatic belt
1990
First airbag fatality - child in front seat
1997
53 deaths from airbag deployment - peak year
1998
FINALLY: Frontal airbags mandatory after 28 years
2000
Advanced airbag rule - sensing, suppression for small occupants

## Slide 25
The Depowering Crisis: When Airbags Killed
Early airbags designed for UNBELTED adult males
Deployed with maximum force in every crash - no modulation
Problem: What about children? What about small adults close to airbag?
1990: First airbag fatality - a child
1996-1997: 53 deaths from airbag deployment
  Victims: mostly children in front seats, small women sitting close
The data-driven fix (1998-2000):
  'Depowered' airbags with lower inflation force
  Weight sensors in seats detect occupant size
  Suppression systems for small occupants
  'Airbag off' indicators
Today: <10 airbag deaths/year vs. ~2,800 lives SAVED per year
The data showed the problem. Better data gave us the solution.

## Slide 26
NHTSA NCAP Frontal Test
NHTSA | Introduced: 1979
PURPOSE
Consumer information program testing at 35 mph - HIGHER than the 30 mph FMVSS requirement. Generates 1-5 star ratings based on injury probability. Created competitive pressure for safety beyond minimum compliance. Industry opposed it as 'unfair' and 'confusing' - but '5-star safety rating' became marketing gold.
KEY MEASUREMENTS
Same as FMVSS 208 but at higher speed
50th male + 5th female dummies
Star ratings based on injury risk curves
Frontal rating contributes to Overall Vehicle Score
DTS CONNECTION
Higher speed = higher forces = more demanding instrumentation requirements. DTS systems must capture data accurately at 35 mph impact severity. Reliability is critical - a single test costs $50-500K, and the published rating affects sales for years.

## Slide 27
IIHS Moderate Overlap Frontal
IIHS | Introduced: 1995
PURPOSE
The problem: Only 25% of real frontal crashes are 'full frontal.' Most are offset - hitting at an angle or with one side of the vehicle. 40% of vehicle width strikes a deformable barrier at 40 mph. Tests structural engagement on ONE side only. Early results shocked the industry - some '5-star' NCAP vehicles performed poorly.
KEY MEASUREMENTS
50th male Hybrid III in driver position
Structural rating (intrusion measurement)
Head/neck injury measures
Chest injury measures (deflection, acceleration)
Hip/leg injury measures
Restraint/kinematics evaluation
DTS CONNECTION
Offset crashes stress structure differently - forces concentrated on one side. DTS instrumentation captures whether the structure held and whether the restraint system kept the occupant in position. Intrusion measurements show if survival space was maintained.

## Slide 28
IIHS Small Overlap Frontal
IIHS | Introduced: 2012
PURPOSE
Only 25% of vehicle width strikes a RIGID barrier at 40 mph. The small overlap bypasses main structural rails - forces go through wheel and suspension into footwell. When introduced, luxury vehicles that passed every other test failed miserably. BMW, Mercedes, Audi - all Marginal or Poor. Forced complete structural redesigns within 3 years.
KEY MEASUREMENTS
50th male Hybrid III in driver position
Structural/safety cage integrity
Footwell intrusion (critical - wheel invasion)
Head trajectory and contact
Dummy kinematics (did occupant stay in position?)
2017: Passenger side added to prevent asymmetric 'gaming'
DTS CONNECTION
The most demanding frontal test. Small overlap creates unique loading - A-pillar rotation, wheel intrusion, occupant sliding toward gap. DTS systems capture head trajectory, torso kinematics, and contact forces. Every channel tells part of the story of whether the structure held and the restraints worked.

## Slide 29
Small Overlap Test (2012): The Shock
What Failed
BMW 3 Series - MARGINAL
Mercedes C-Class - MARGINAL
Audi A4 - MARGINAL
Lexus IS - MARGINAL
Lexus ES - MARGINAL
Lincoln MKZ - POOR
Buick Regal - POOR
Volkswagen CC - POOR
What It Revealed
These were luxury vehicles that earned
top marks in every other test.
The small overlap exposed a
critical structural blind spot.
Within 5 years, most redesigns
earned GOOD ratings.
The test drove real engineering change.

## Slide 30
Side Impact Testing
The door that wasn't a barrier

## Slide 31
25% / 30%
Side impacts: 25% of crashes but 30% of fatalities
More deadly PER CRASH than frontal because: minimal crush space, no crumple zone, direct loading to occupant's torso and head

## Slide 32
FMVSS 214: Side Impact Protection
NHTSA | Introduced: 1973 (static) / 1990 (dynamic)
PURPOSE
Originally a static door strength test (1973). Dynamic MDB test added 1990 - moving deformable barrier strikes stationary vehicle at 33.5 mph, 90 degrees. 2007: Pole test added (254mm pole at 20 mph) to drive side curtain airbag adoption for head protection. The pole test specifically targets head injury - tree strikes, utility poles.
KEY MEASUREMENTS
ES-2re dummy (50th male side impact)
Thoracic Trauma Index (TTI)
Pelvis acceleration
Rib deflection (Viscous Criterion)
Head injury (HIC for pole test)
Lower spine acceleration
DTS CONNECTION
Side impact dummies are fundamentally different from frontal dummies - different rib structure, different instrumentation. DTS rib deflection sensors, accelerometers at multiple locations. The pole test head measurements drove universal adoption of side curtain airbags - now standard equipment.

## Slide 33
The Side Airbag Revolution
Pre-1995
Nothing between your ribs and the door in a side crash
1995
Volvo introduces first side torso airbag
1998
First side curtain airbags (head protection)
2003
IIHS side test launched - accelerates adoption
2007
FMVSS 214 pole test requires head protection
2010
Side curtain airbags standard on most vehicles
2021
IIHS updates side test: heavier, taller, faster barrier

## Slide 34
IIHS Side Impact (Original 2003, Updated 2021)
IIHS | Introduced: 2003 / 2021
PURPOSE
Original (2003): 31 mph MDB strike using SID-IIs (5th percentile female) dummy - focused on protecting smaller occupants. Updated (2021): 37 mph strike with heavier (4,200 lb vs 3,300 lb), taller barrier simulating modern SUVs and trucks. Many vehicles that earned 'Good' with old test dropped to lower ratings with new test.
KEY MEASUREMENTS
SID-IIs (small female) in front row
Head injury criterion (HIC)
Thorax injury (chest deflection, TTI)
Pelvis injury
Structural intrusion measurement
Updated barrier: Taller profile matches SUV/truck front ends
DTS CONNECTION
The 2021 update reflects fleet changes - SUVs and trucks now dominate. Higher, heavier barrier creates different loading. DTS instrumentation must perform reliably at higher energy levels. The small female dummy choice protects the most vulnerable - not just the 'average' male.

## Slide 35
Rollover & Roof Strength
When the sky falls

## Slide 36
3% / 30%
Rollovers: 3% of crashes but 30% of fatalities
Ejection in rollover is 77% fatal. SUVs had higher rollover rates due to high center of gravity. The mechanism is different - multiple impacts, occupant not restrained against a surface.

## Slide 37
FMVSS 216: Roof Crush Resistance
NHTSA | Introduced: 1973 / 2009 upgrade
PURPOSE
Static test: metal plate pressed onto roof at windshield/roof junction at 5-degree angle. Original (1973): roof must withstand 1.5x vehicle weight. This standard was unchanged for 36 YEARS despite advocacy for stronger roofs. Upgraded (2009): doubled to 3x vehicle weight, both sides tested. IIHS pushed further: 4x required for 'Good' rating.
KEY MEASUREMENTS
Force vs. displacement measurement
Peak force before 127mm (5 inches) of crush
Both left and right sides tested (post-2009)
DTS load cells measure applied force
Displacement sensors track crush
DTS CONNECTION
Unlike crash tests, roof strength is a static test - controlled force application. DTS load cells and displacement sensors capture the force-deflection curve. The test determines if occupants have survival space if the vehicle rolls. Many modern vehicles exceed 5-6x ratios.

## Slide 38
Electronic Stability Control: Preventing the Rollover
Roof strength protects IN rollovers
ESC PREVENTS rollovers from happening
How it works:
  Sensors detect loss of control (compares steering input to actual direction)
  System applies individual brakes to correct
  Acts in milliseconds - faster than human reaction
FMVSS 126: ESC required on all vehicles by 2012
Effectiveness: 75% reduction in fatal single-vehicle rollovers
Combined with side curtain airbags (prevent ejection):
  Rollover fatalities dropped dramatically
This is active safety + passive safety working together
You prevent the rollover with ESC. If one happens anyway, the strong roof and curtain airbags protect you.

## Slide 39
Rear Impact & Whiplash
The hidden epidemic

## Slide 40
IIHS Head Restraint / Whiplash Test
IIHS | Introduced: 1995 (geometry) / 2004 (dynamic)
PURPOSE
Over 1 MILLION whiplash injuries per year in US. Most occur in low-speed rear impacts. Early head restraints were set too low and too far back - didn't engage head before neck stretched. Swedish research led to 'active' head restraints that move up/forward during crash. Dynamic test (2004) uses BioRID II dummy with highly articulated spine.
KEY MEASUREMENTS
BioRID II dummy - 24 articulated vertebrae
Neck injury criteria (NIC)
Neck forces and moments
Relative head-to-torso movement
Seat strength (must not collapse backward)
DTS CONNECTION
Whiplash isn't fatal but has enormous economic impact - medical costs, lost work, chronic pain. BioRID II spine instrumentation captures the neck dynamics that cause injury. DTS sensors along the articulated spine measure relative motion. Active head restraints now standard because of this test.

## Slide 41
Fuel System Integrity
The Ford Pinto scandal

## Slide 42
FMVSS 301: When Cost-Benefit Analysis Failed
Post-crash fires were killing people in survivable crashes
Ford Pinto (1971-1980): Rear fuel tank 6 inches from bumper
  Could rupture in rear impacts
  Bolts on differential could puncture tank
The infamous internal memo (1973):
  Fix cost: $11/car x 12.5 million vehicles = $137 million
  'Acceptable' deaths: 180 x $200,000 = $36 million
  FORD CHOSE NOT TO FIX THE DESIGN
The reckoning:
  1977: Mother Jones 'Pinto Madness' expose
  1978: Recall of 1.5 million Pintos
  1978: First criminal prosecution of an automaker
FMVSS 301 strengthened in direct response
Estimated 27-180 deaths from this single design decision

## Slide 43
FMVSS 301: Fuel System Integrity
NHTSA | Introduced: 1968 / 1977 upgrade
PURPOSE
Tests fuel system in multiple crash modes: rear impact (30 mph MDB), frontal impact (30 mph barrier), side impact (20 mph MDB), and rollover (90 and 180 degree). Measures fuel leakage during and after crash. The Pinto scandal drove significant tightening of leakage limits and test severity in 1977.
KEY MEASUREMENTS
Fuel leakage measurement during impact
Fuel leakage measurement post-crash (30 min)
Tank attachment integrity
Fuel line integrity
Static rollover test
DTS CONNECTION
Not a dummy instrumentation test - fuel leakage measurement. But crash severity must be verified. DTS accelerometers on vehicle structure confirm impact severity. This test ensures survivable crashes don't become fatal due to fire.

## Slide 44
Active Safety
From surviving crashes to preventing them

## Slide 45
The Philosophy Shift
Passive Safety (1968-2000s)
Assume crash WILL happen
Focus on protection DURING crash
- Seatbelts
- Airbags
- Structure
After 50 years, we've gotten very good
at protecting people in crashes.
But 94% of crashes involve human error...
Active Safety (2000s-present)
Try to PREVENT the crash
Warn driver, assist, brake automatically
- AEB (Autonomous Emergency Braking)
- ESC (Electronic Stability Control)
- Lane Keeping Assist
- Blind Spot Monitoring
If crash unavoidable, passive kicks in.
Active + Passive = Maximum protection

## Slide 46
IIHS Front Crash Prevention (AEB)
IIHS | Introduced: 2013
PURPOSE
Tests Autonomous Emergency Braking effectiveness. Vehicle approaches stationary foam target at 12 mph and 25 mph. Measures: Does it warn? Does it brake automatically? How much speed reduction? Ratings: Superior / Advanced / Basic. In 2016, 20 automakers voluntarily committed to make AEB standard by 2022 - the fastest safety technology adoption in history.
KEY MEASUREMENTS
Vehicle approach speed
Warning timing
Brake application timing
Speed at impact (or full stop)
Target must be stationary foam vehicle
DTS CONNECTION
Not traditional crash test instrumentation, but a growing market. DTS expanding into vehicle dynamics measurement. AEB reduces rear-end crashes by 50%+. The future of safety testing includes evaluating systems that PREVENT crashes.

## Slide 47
The Pedestrian Crisis: When Occupant Safety Isn't Enough
While occupant deaths have FALLEN, pedestrian deaths are RISING:
  2009: 4,109 pedestrian deaths
  2019: 6,205 pedestrian deaths
  2022: 7,500+ pedestrian deaths (18% of all traffic deaths)
Why?
  Larger vehicles (SUVs, trucks) dominate sales
  Higher front ends hit torso/head instead of legs
  Distracted driving and walking
IIHS Pedestrian AEB testing (2019):
  Adult and child pedestrian targets
  Day and night scenarios
  Crossing and parallel walking
Euro NCAP has tested pedestrian PROTECTION (hood impact) since 1997
US has NO federal pedestrian crashworthiness standard
We've gotten very good at protecting people INSIDE vehicles. Now we must protect people OUTSIDE.

## Slide 48
Euro NCAP Pedestrian Protection
Euro NCAP | Introduced: 1997
PURPOSE
Europe has tested pedestrian protection for 25+ years while US has no federal standard. Uses impactors - headform and legform fired at vehicle surfaces. Headform tests hood and windshield base. Legform tests bumper. Drove design changes: active hood hinges, energy-absorbing bumpers, external pedestrian airbags (Volvo). The US tests if cars AVOID pedestrians (AEB) but not what happens if they don't.
KEY MEASUREMENTS
Headform impactor (adult and child sizes)
- Fired at hood surface at 40 km/h
- HIC measurement
Upper legform impactor
- Fired at bumper/leading edge
- Bending moment, shear force
Lower legform impactor
- Knee bending, shear, acceleration
DTS CONNECTION
Headform impactor testing uses DTS accelerometers inside the impactor headform - same basic technology as crash dummies. The physics is identical: protect the brain from rapid deceleration. Expanding market as US considers pedestrian protection requirements.

## Slide 49
Beyond Automotive
Same physics, different arena

## Slide 50
The Concussion Crisis in Sports
2005: Dr. Bennet Omalu publishes first CTE case in NFL player (Mike Webster)
2009: NFL finally acknowledges concussion problem after years of denial
2011: $765 million settlement with former players
The science:
  Concussion: Brain injury from rapid deceleration
  CTE: Degenerative disease from REPEATED impacts
  Even 'subconcussive' impacts accumulate
The question: Can better helmets reduce brain injury?
Same question we answer in automotive: How do we protect the head?
Same injury criterion: Severity Index closely related to HIC
Same measurement: Accelerometers on the head

## Slide 51
NOCSAE Football Helmet Testing
NOCSAE | Introduced: 1973
PURPOSE
Founded after 36 football fatalities in 1968. Drop tower test: helmet on headform dropped from 60 inches onto various anvils. Severity Index must be below 1200. Later added linear impactor testing (2016) - ram fired at helmet to simulate player-to-player collisions. Modern research focuses on rotational acceleration (may be more important than linear for brain injury).
KEY MEASUREMENTS
Headform acceleration (triaxial)
Severity Index < 1200
Multiple drop locations
Hot, cold, wet conditions
Linear impactor: 20+ mph impacts
Rotational measurements (emerging)
DTS CONNECTION
DTS accelerometers inside helmet headforms - same sensors used in automotive crash dummies. The injury threshold (SI < 1200) is derived from the same human tolerance research as automotive HIC. One technology, one data acquisition approach, applied across domains.

## Slide 52
90%
Reduction in football fatalities since NOCSAE standards (1973)
1960s: 26 deaths/year | 1970s: 15 deaths/year | 2010s: 3 deaths/year Better helmets, better rules, better data.

## Slide 53
Military: Blast Protection & Survivability
IEDs (Improvised Explosive Devices) - leading cause of US casualties in Iraq/Afghanistan
Underbody blast: explosive under vehicle floor
Traditional crash dummies not designed for this loading:
  Vertical acceleration, not horizontal
  Lumbar spine and pelvis critical
  Different injury mechanisms
WIAMan (Warrior Injury Assessment Manikin):
  Developed by US Army with DTS partnership
  Purpose-built for underbody blast testing
  Lumbar spine and pelvis instrumentation
  ~$500,000 per dummy
Same principle: Understand the forces, measure them accurately, engineer protection
DTS partnered with US Army to develop WIAMan - our technology protecting soldiers

## Slide 54
The Future
What gaps remain?

## Slide 55
Every Test Exposed What Previous Tests Missed
1968: FMVSS 208 (frontal) - but side crashes were neglected
1990: FMVSS 214 (side) - but offset frontal crashes were missed
1995: IIHS Moderate Overlap - but small overlap was missed
2012: IIHS Small Overlap - but passenger side was 'gamed'
2017: Small Overlap Passenger - but fleet changed (bigger SUVs)
2021: Updated Side Test - but gaps remain...
What's NEXT?
  Rear seat occupant protection (currently neglected)
  Far-side impacts (opposite side from impact)
  Vehicle compatibility (small cars vs. large trucks)
  EV-specific tests (battery safety, mass distribution)
  AV/ADAS validation (how do you test a self-driving car?)
The cycle continues. New gaps emerge. New tests will be created.

## Slide 56
The Gender Gap in Crash Testing
Most crash tests use 50th percentile male dummy (5'9", 175 lbs)
'Small female' dummy (Hybrid III 5th) is just a SCALED-DOWN male
Women are 17% more likely to DIE in equivalent crashes
Women are 73% more likely to be seriously injured
Why?
  Female anatomy differs: hip structure, neck strength, breast tissue
  Women sit closer to steering wheel (shorter legs)
  Seatbelt geometry optimized for male torsos
The solution (in progress):
  THOR-5F (2023): First 'true female' dummy - not scaled male
  Different skeletal structure, includes breast representation
  NHTSA considering requiring female dummy in tests
Quote: 'For decades, the average human in crash testing has been male.'

## Slide 57
The ATD Evolution: From Sierra Sam to THOR
1949: Sierra Sam - first crash test dummy (USAF ejection seats)
1968: VIP-50 - built for GM and Ford
1971: Hybrid I - GM combined best features
1972: Hybrid II - first FMVSS-compliant dummy
1976: Hybrid III - STILL the global standard for frontal impact
2000s: WorldSID - international side impact harmonization
2013: THOR-50M - advanced male, 150+ data channels
2015: WIAMan - military blast (DTS partnership)
2023: THOR-5F - first true female dummy
The trend: More biofidelic, more instrumentation, more data
Hybrid III: ~47 channels | THOR: 150+ channels
More channels = more data = better understanding = safer designs

## Slide 58
DTS: The Nervous System of Safety Testing
ATDs are mechanical bodies - they can't 'feel' or 'report'
DTS provides the nervous system:
  Accelerometers measure deceleration (head, chest, pelvis)
  Load cells measure forces (neck, femur, tibia)
  Potentiometers measure displacement (chest deflection)
  Angular rate sensors measure rotation
Where DTS equipment is used:
  Every major automotive safety lab worldwide
  NHTSA, IIHS, Euro NCAP
  Every major OEM
  Universities, research institutions
  Military (WIAMan partnership)
  Sports (helmet testing)

## Slide 59
"A crashed car is gone forever. The data is what remains."
-- Industry saying

## Slide 60
Why Data Quality Matters
A single crash test costs $50,000 - $500,000+
  Test vehicle: $30,000 - $80,000 (destroyed)
  ATD (Hybrid III 50th): $200,000 - $400,000
  ATD (THOR): $500,000 - $800,000
  Facility, personnel, analysis
The vehicle is destroyed in 100 milliseconds
ALL VALUE is captured in the data
If a sensor fails, if a channel drops, if data is questionable:
  You might have to repeat the entire test
  $100K+ repeat cost, weeks of delay
DTS data acquisition is a fraction of test cost
But it captures 100% of the value
Our customers demand reliability because the stakes are that high

## Slide 61
The Data Chain: From Impact to Insight
Frontal crash: Head, chest, femur loads - DTS instrumentation
Side crash: Pelvis, thorax, head loads - DTS instrumentation
Roof crush: Force vs. displacement - DTS load cells
Sled tests: Dummy kinematics - DTS systems
Pedestrian impactors: Headform acceleration - DTS accelerometers
Helmet testing: Same accelerometers, same DAQ
Military blast: WIAMan instrumentation - DTS partnership
Test methods evolve. Pass/fail thresholds change.
Vehicles change. Regulations change.
DATA REQUIREMENTS REMAIN.
DTS provides the data that makes every test meaningful.

## Slide 62
The Bottom Line
Why this matters

## Slide 63
117,000
Lives saved per year compared to 1970 rates
1970 fatality rate applied to today's VMT: 153,000 deaths per year Actual 2019 deaths: 36,000 | Difference: ~117,000 lives per year

## Slide 64
Each of Those Lives Was Saved By:
A TRAGEDY that revealed a problem
  Steering column deaths, Pinto fires, football fatalities
PIONEERS who asked 'why?' and investigated
  DeHaven, Stapp, Bohlin, Patrick, Haddon, Nader
INSTITUTIONS that were formed or empowered
  NHTSA, IIHS, NOCSAE, Euro NCAP
DATA that revealed the mechanism of injury
  Cadaver research, rocket sled tests, crash tests
A TEST that measured the problem
  FMVSS 208, IIHS Small Overlap, NOCSAE drop test
ENGINEERING that solved it
  Seatbelts, airbags, crumple zones, helmets
DTS is in this chain at steps 4, 5, and 6 - capturing the data that drives solutions

## Slide 65
The Work Continues
The cycle hasn't stopped:
  Pedestrian deaths are RISING while occupant deaths fall
  Rear seat occupants are less protected than front
  Female occupants are more likely to die than males
  Autonomous vehicles create new testing challenges
New tragedies will reveal new gaps
New institutions will form or expand
New tests will be created
New data will be required
And DTS will be there - providing the instrumentation,
the data acquisition, the accuracy and reliability
that turns crashes into knowledge and knowledge into lives saved.

## Slide 66
Data Saves Lives
Every test has a story. Every story started with tragedy. Every tragedy ended when we got the data to understand it.

## Slide 67
Questions?
DTS: The data that makes safety testing possible.